## Slide 1
SNN for Environmental Sound Classification on ESC-50
COMP30040 Thesis Progress Update
Ayush Kumar
March 2026

## Slide 2
Project Recap
First application of Spiking Neural Networks to the ESC-50 dataset
Research question: How do different spike encoding methods affect SNN performance on environmental sound classification?
Compare 4 encoding methods: rate, delta, latency, direct
Measure accuracy vs ANN baseline + energy consumption

## Slide 3
ESC-50: Environmental Sound Classification
2,000 audio clips | 5 seconds each | 50 classes | 40 clips per class
5 predefined folds for cross-validation
Category | Example Classes
Animals | dog, cat, rooster, cow, frog, pig, hen, insects, sheep, crow
Nature / Water | rain, sea waves, fire, crickets, birds, wind, thunderstorm
Human (non-speech) | crying baby, sneezing, clapping, laughing, coughing
Interior / Domestic | keyboard, mouse click, door knock, vacuum, washing machine
Exterior / Urban | helicopter, chainsaw, siren, car horn, airplane, train

## Slide 4
Processing Pipeline
5-sec WAV Audio
Mel Spectrogram (64 x 216 image)
Spike Encoding
SNN Classification
Mel spectrogram: breaks audio into time-frequency representation, uses mel scale matching human hearing
64 mel frequency bins x 216 time frames = audio treated as a greyscale image
Spike encoding converts this image into binary spike trains for the SNN

## Slide 5
Network Architecture (SNN & ANN)
Layer / Operation | What It Does
Layer 1: Conv2d(1 → 32) | 32 small 3×3 filters scan the spectrogram detecting basic patterns
BatchNorm + MaxPool(2) | Normalise, then shrink by half (64×216 → 32×108)
LIF neuron (SNN) / ReLU (ANN) | SNN: accumulates input, fires binary spike when threshold crossed. ANN: just outputs max(0, x)
Layer 2: Conv2d(32 → 64) | 64 filters detect higher-level pattern combinations
BatchNorm + MaxPool(2) | Shrink again (32×108 → 16×54)
AvgPool(4, 6) | Compress to 4×9 = 2,304 features
FC: 2304 → 256 → 50 | Classify into 50 sound classes
Both models have identical structure; only activation differs (LIF vs ReLU)

## Slide 6
Why This Architecture?
Conv layers (32→64 filters, 3x3 kernels):
• Followed standard CNN audio classification patterns
• Filter doubling (32→64) is a common convention from VGGNet
• 2 conv layers keeps it simple — deeper nets need more data than ESC-50’s 1,600 training samples
LIF neuron parameters:
• beta=0.95 and 25 timesteps from snnTorch tutorials (Eshraghian et al.)
• beta=0.95 means the neuron retains 95% of its voltage each step — reasonable decay rate
• 25 timesteps balances temporal dynamics vs training speed
Mel spectrogram (64 bins, hop=512, sr=22050):
• Standard librosa defaults for audio classification
• 64 mel bins is the most common choice in existing ESC-50 ANN work
• 22050 Hz is enough for environmental sounds
Training setup (Adam, lr=1e-3, early stopping):
• Standard deep learning defaults — nothing exotic here
• No hyperparameter search done; focus was on the SNN vs ANN comparison, not tuning
Bottom line: mostly snnTorch tutorials + standard audio ML conventions. Room to improve with proper hyperparameter optimisation.

## Slide 7
Progress: Completed Work
✓ Data pipeline: WAV → mel spectrogram → PyTorch tensors
✓ ANN baseline trained (5-fold CV on CSF3 A100 GPUs)
✓ SNN trained with 4 encoding methods (5-fold CV each)
✓ Energy analysis: SynOps vs MACs comparison
✓ Confusion matrices + per-class accuracy for all experiments
✓ SpiNNaker deployment in progress (live on real hardware)
✓ Literature review of SNN audio classification landscape

## Slide 8
Classification Accuracy (5-Fold CV)
Model | Encoding | Mean Accuracy | Std
ANN | — | 63.85% | ±3.07%
SNN | Direct | 47.15% | ±4.50%
SNN | Rate | 24.00% | ±1.90%
SNN | Latency | 16.30% | ±1.62%
SNN | Delta | 7.25% | ±0.94%
Direct encoding (no spike conversion) performs best. Random chance = 2%.
All training done on university CSF3 cluster with NVIDIA A100 GPUs

## Slide 9
SNN Audio Classification: Where We Fit
Dataset | Task | Best SNN Acc | Reference
SHD | Spoken digits | 96.4% | Bittar & Garner 2022
RWCP | Indoor sounds (19 classes) | 99.6% | Wu et al. 2020
TIDIGITS | Digit recognition | 97.5% | Dong et al. 2023
Google Speech | Keyword spotting (35 classes) | 95.1% | Stewart et al. 2023
UrbanSound8K | Urban sounds (10 classes) | ~75% | Various
ESC-10 | Env. sounds (10 classes) | 66.1% F1 | Dennis et al. 2013
ESC-50 | Env. sounds (50 classes) | 47.15% (ours) | First SNN attempt
ESC-50 is harder: 50 classes vs 10–35 in prior work, and sounds are more diverse

## Slide 10
Energy Comparison: SNN vs ANN
SNN (Software Simulation)
1.51 billion SynOps per sample
0.9 pJ per SynOp (Loihi estimate)
Total: 1,358 million pJ
ANN (Traditional)
68.3 million MACs per sample
4.6 pJ per MAC (45nm CMOS)
Total: 314 million pJ
pJ (picojoule) = 10⁻² joules — standard unit for per-operation energy
SynOp = when a spike travels along a synapse (SNN operation)
MAC = multiply-accumulate (ANN operation)
SNN uses 4.3× MORE energy in software simulation. But neuromorphic hardware (Loihi, SpiNNaker) processes spikes event-driven — only computing when spikes occur — which is where real savings emerge.

## Slide 11
What We've Learned
-Direct encoding works best because it lets the network learn its own temporal coding
-Rate encoding (24%) shows temporal information helps but naive conversion loses spatial structure
-Delta encoding (7.25%) near-random — change-based coding doesn't suit spectrograms well
-SNN accuracy gap vs ANN (47% vs 64%) is expected — consistent with literature (SNNs trade accuracy for efficiency)
-Energy results show software simulation doesn't capture event-driven efficiency
-The real energy advantage requires neuromorphic hardware (SpiNNaker deployment in progress)

## Slide 12
SpiNNaker Deployment – What We Did
Deployment strategy: FC-only hybrid approach
  Conv features extracted on CPU (offline preprocessing)
  FC classifier (2304 → 256 → 50 LIF neurons) deployed to SpiNNaker
  SpiNNaker1 doesn't support Conv2d natively → hybrid approach is standard
Language: Python (via PyNN / sPyNNaker library)
Hardware: SpiNN-5 board (48 ARM968 cores/chip, 47-48 chips/board)
Access: Remote via spalloc server at spinnaker.cs.man.ac.uk (Univ. of Manchester)
Software stack: sPyNNaker 7.4.1, PyNN 0.12.4, SpiNNMan 7.4.1
Documentation sources:
  Official sPyNNaker docs: spinnakermanchester.github.io
  PyNN documentation (standardised SNN simulator API)
  SpiNNaker GitHub repos (SpiNNakerManchester org)
  sPyNNaker tutorials and examples

## Slide 13
SpiNNaker – Parameter Mapping Challenge
snnTorch model uses snn.Leaky (LIF neuron):
  beta = 0.95, threshold = 1.0, reset = 0
  V[t+1] = 0.95 * V[t] + I (direct current injection)
sPyNNaker uses IF_curr_exp neuron model:
  tau_m = 20.0ms (gives beta ≈ 0.951 via exp(−1/20))
  v_thresh = 1.0, v_reset = 0.0, v_rest = 0.0
  BUT: has exponential synaptic current decay (tau_syn_E/I)
  Current decays BEFORE reaching membrane → effective input is weaker
Weight conversion:
  snnTorch weights → (pre_idx, post_idx, weight, delay) format
  Excitatory/inhibitory weights separated (sPyNNaker requirement)

## Slide 14
SpiNNaker – Run Results & Errors
Run 1 (20 samples): 0% accuracy (0/20 correct)
  Input spikes active: 17,000 – 35,000 per sample
  Hidden layer spikes: 0 (complete signal death)
  Output layer spikes: 0 → every sample defaults to prediction = class 0
Run 2 (20 samples): 0% accuracy – confirms systematic issue
Run 3: Crashed with OSError: [Errno 55] No buffer space available
  UDP buffer overflow when loading 451K connections to the board
  Weight pruning at threshold=0.005 retained 80% of connections (too many)
  SpinnmanIOException: Error sending: [Errno 55] No buffer space available
Key Error Codes from Logs:
  WARNING: "Danger of SpikeSourceArray sending too many spikes at the same time"
    e.g. at time 23.0, 1398 spikes will be sent simultaneously
  ERROR: "Could not read the status count – going to individual cores"
  WARNING: "Could not read information from 23 cores"
  SpinnmanTimeoutException: Operation SCPCommand.CMD_NNP timed out (1.0s)

## Slide 15
SpiNNaker – Root Cause Analysis & Next Steps
Root Causes Identified:
1. Synaptic current model mismatch: snnTorch has NO synaptic current decay; sPyNNaker IF_curr_exp has exponential decay. Current decays before membrane integration
2. Weight scale: Trained weights are too small for sPyNNaker's current dynamics → neurons never reach threshold (V < 1.0)
3. Connection overload: 451K connections overflows UDP buffer during transfer. Need more aggressive pruning (threshold > 0.05)
4. Spike flooding: ~1400 simultaneous spikes per timestep exceeds SpiNNaker's packet routing capacity
What to Try Next:
Increase weight scale (multiply all weights by 2–5x)
Use tau_syn_E = tau_syn_I = 0.1 (near-instantaneous, closer to snnTorch)
More aggressive weight pruning (threshold = 0.1+)
Reduce input dimensionality (PCA on conv features before SpiNNaker)
Try IF_curr_delta neuron model (no exponential current decay at all)

## Slide 16
SpiNNaker – Questions for Dr. Rhodes
Is IF_curr_delta available on SpiNNaker? Would it better match snnTorch's direct current injection model?
Should we scale weights empirically (grid search) or derive a theoretical correction factor from the tau_syn mismatch?
Is the FC-only hybrid deployment sufficient for the thesis, even without achieving working accuracy on SpiNNaker?
Are there published snnTorch-to-sPyNNaker weight transfer protocols we should be following?

## Slide 17
SpiNNaker – Hardware Verification
Confirmed: Real SpiNNaker neuromorphic hardware (not a simulator)
Key Evidence:
SC&MP 4.0.0 firmware read from physical chip (simulators return fake 3.4.2)
47-48 chips detected per board (one faulty chip = real hardware; simulators show perfect 48)
836-855 ARM968 cores per board, 118MB SDRAM per chip
Different physical boards allocated across runs (10.11.219.97, .177, .49, .113)
Network & Identity:
DNS/WHOIS: spinnaker.cs.man.ac.uk → 130.88.193.57 → University of Manchester, Kilburn Building
On-chip IOBUF firmware logs from individual ARM968 processors
27-37 second board setup time (real network latency, not instant)

## Slide 18
Next Steps
▶ Complete SpiNNaker inference and compare hardware vs software energy
▶ Per-class analysis: which sound categories do SNNs handle well/poorly?
▶ Explore architecture improvements (deeper networks, attention mechanisms)
▶ Begin thesis report writing (Background, Methodology, Results chapters)
▶ Statistical significance testing across folds

## Slide 19
Improving SNN Accuracy (Beyond 47%)
SpiNNaker will reproduce the same ~47% accuracy if mapping works. To push higher:
Highest Impact (Easy):
• Data augmentation — SpecAugment, time shift, mixup, noise injection
(We currently use none. 1,600 training samples → overfitting is likely)
• Longer training — cosine annealing schedule, 100+ epochs
(Currently max 50 epochs with early stopping)
Architecture Changes:
• Deeper network — add 3rd conv layer (Conv2d 64→128)
(Current ~622K params is small; deeper ANNs hit 80%+ on ESC-50)
• More timesteps — increase from 25 to 50–100
(More time for temporal integration, at cost of training speed)
Advanced:
• Learnable encoding layer — trainable spike generator instead of repeating spectrogram
• Transfer learning — pre-trained audio features (VGGish/PANNs) + SNN classifier
• Membrane potential readout — weighted combo of spike count + final voltage
Most practical next step: data augmentation + longer training

## Slide 20
References & Further Reading
Papers & Research:
Piczak, K.J. (2015). ESC: Dataset for Environmental Sound Classification. ACM MM.
arXiv 2503.11206 (2025). Confirms no prior SNN work on ESC-50.
Eshraghian, J.K. et al. (2023). Training Spiking Neural Networks Using Lessons from Deep Learning. Proc. IEEE.
Bittar, A. & Garner, P.N. (2022). A surrogate gradient spiking baseline for speech command recognition. Front. Neurosci.
Wu, J. et al. (2020). A Tandem Learning Rule for Effective Training and Rapid Inference of Deep SNNs. arXiv.
Horowitz, M. (2014). Computing's Energy Problem. ISSCC. [Energy per MAC: 4.6 pJ at 45nm]
Davies, M. et al. (2018). Loihi: A Neuromorphic Manycore Processor. IEEE Micro. [Energy per SynOp: 0.9 pJ]
Furber, S.B. et al. (2014). The SpiNNaker Project. Proc. IEEE.
Rhodes, O. et al. (2018). sPyNNaker: A Software Package for Running PyNN Simulations on SpiNNaker. Front. Neurosci.
Rowley, A. et al. (2019). SpiNNTools: The Execution Engine for the SpiNNaker Platform. Front. Neurosci.
Software & Tools:
snnTorch 0.9.4 -- github.com/jeshraghian/snntorch
sPyNNaker 7.4.1 -- github.com/SpiNNakerManchester
PyNN 0.12.4 -- neuralensemble.org/PyNN
PyTorch 2.6 -- pytorch.org
librosa -- librosa.org (audio/mel spectrogram processing)
ESC-50 Dataset -- github.com/karolpiczak/ESC-50
SpiNNaker Documentation:
spinnakermanchester.github.io -- Official sPyNNaker docs
spalloc.readthedocs.io -- Board allocation system
SpiNNaker Wikipedia -- en.wikipedia.org/wiki/SpiNNaker

## Slide 21
Questions?
Project repo: snn-esc50/
Trained on: CSF3 (A100 GPUs) + SpiNNaker (neuromorphic hardware)
Tools: snnTorch, librosa, PyTorch, sPyNNaker